## Slide 1: Mugi Value Level Parallelism For Efficient LLMs
Daniel Price, Prabhu Vellaisamy*, John P. Shen*, Di Wu
UCF, CMU*

## Slide 2: AI–Hardware Scaling Gap
Model parameters increasing
Hardware scaling lags
Hardware efficiency stagnates
https://hai.stanford.edu/ai-index/2025-ai-index-report
Notes: Parameter counts growing Hardware throughput growing slower Energy efficiency nearly stagnant
How can we improve throughput and efficiency at the same time?

## Slide 3: LLMs and VLP
LLM challenges
Opportunities
Nonlinear operations in LLMs
Value level parallelism (VLP)

## Slide 4: Challenges for LLM Inference
 | DNN | LLM
1. Operations beyond GEMM (Nonlinear) | Simple | Complex
2. Weight/Activation datatypes | Symmetric | Asymmetric
 | Existing Architecture | Mugi
3. Batch Size | Large batch | Small batch
4. Operations beyond GEMM (Nonlinear) | Separate GEMM/nonlinear hardware | Integrated
Notes: DNN contains simple nonlinear (relu) LLM contains complex nonlinear (softmax, silu)
DNN weights and activations are symmetric (same size) LLM are asymmetric (weight only quantization popular option)
DNN small weights large batch LLM large weights small batch
Hardware for nonlinear and gemm separate

## Slide 5: Nonlinear Operations in LLMs
Existing solution
  Precise computation
    Costly
  Hardware approximations
    Taylor series, piece-wise linear, etc.
    Inaccurate

## Slide 6: Opportunity – Small Batch GEMM in LLMs
Small batch decoding
  e.g., 8~16
GQA for KV Cache GEMM
Notes: Small batch GEMMs in LLMs
General hardware are underutilized
This small batch size aligns with Mugi row width to fully saturate the array
GQA converts attention from GEMV to GEMM, shown in next slide

## Slide 7: Opportunity – Group Query Activation
Multi-head attention
  1 token
  Low utilization
Group query attention
  Multiple key/value pairs
  Reduces KV cache size
  Increases utilization
  KV Cache quantization
    INT4
Notes: GQA shares key value groups to multiple querys
Reduces kv cache size
Increases util by converting to GEMM
Common size of 8 aligns with batch size, thus aligns with mugi array
KV cache can be quantized, discussed in next slide

## Slide 8: Opportunity – Weight Only Quantization
Large weight matrices
  Quantize weight
    INT4 = 16 possible values
  Full precision activation
KV Cache quantization
  Aligns with WOQ
Notes: WOQ decreases the large weight matrices size
Decreases memory requirements
Reduces possible value range
Leveraged by VLP

## Slide 9: Value Level Parallelism
First proposed in Carat, ASPLOS 2O24
  Beneficial at lower bitwidth
Vector dimension 1024, UINT4 data format
Only 16 unique products
1024/16=64x more than necessary
Notes: First proposed in ASPLOS 2024
16 possible products
Can there be any value reuse?

## Slide 10: Value Level Parallelism
Temporal subscription
  Select output when cycle matches input
  Empowered by small value range
VLP multiplication
  TC converts w to spike
  Accumulation over n cycles
  VLP subscribes product

## Slide 11: VLP Vectorization
Value reuse
  Rows share column values
VLP array
  Multiple Columns
  Column width of 8
    2^bitwidth
Notes: UINT4 without sign is 8 possible values

## Slide 12: Mugi
Nonlinear approximation
Small batch, low precision GEMM
Unified architecture

## Slide 13: VLP for Nonlinear Approximation
LUT
  Precompute and store costly nonlinear operations
Standard LUT
  Doesn't allow parallel accesses
Two stage spatial LUT
  Sign-Mantissa subscription
  Exponent subscription

## Slide 14: VLP for Nonlinear Approximation
LUT
  Precompute and store costly nonlinear operations
Standard LUT
  Doesn't allow parallel accesses
Two stage spatial LUT
  Sign-Mantissa subscription
  Exponent subscription

## Slide 15: VLP for Nonlinear Approximation
LUT
  Precompute and store costly nonlinear operations
Standard LUT
  Doesn't allow parallel accesses
Two stage spatial LUT
  Sign-Mantissa subscription
  Exponent subscription

## Slide 16: VLP for Nonlinear Approximation
LUT
  Precompute and store costly nonlinear operations
Standard LUT
  Doesn't allow parallel accesses
Two stage spatial LUT
  Sign-Mantissa subscription
  Exponent subscription
Notes: Row width of 8, more than 8 exponents

## Slide 17: Selecting a Window
Mugi array < LUT row
  Select a window by the minimum exponent
  Outlier values processed (rounded, truncated)

## Slide 18: VLP Approximation
Four phases
  Input field split (approximation)
  Value reuse
  Mantissa temporal subscription
  Exponent temporal subscription

## Slide 19: VLP Approximation
1. Input field split (approximation)

## Slide 20: VLP Approximation
2. Value reuse

## Slide 21: VLP Approximation
3. Mantissa temporal subscription

## Slide 22: VLP Approximation
4. Exponent temporal subscription

## Slide 23: Mugi Architecture
- corresponds to the four phases of VLP approximation
  Purple: Accumulation and vector computation
  Red: Activation and LUT loading
  Yellow: weight and nonlinear loading
  Green: Compute array
  Blue: Postprocessing
1
4
Notes: Make dark circles to align with figure

## Slide 24: Mugi GEMM Mapping
Activations feed into columns
Weights feed into rows

## Slide 25: Mugi GEMM Mapping
Compute array subscribes to accumulated values

## Slide 26: Mugi GEMM Mapping
Accumulate output tiles

## Slide 27: Mugi GEMM Mapping
Accumulated tiles are scaled and stored
Notes: Remove outline

## Slide 28: Mugi Nonlinear Mapping

## Slide 29: Mugi Nonlinear Mapping
Input field split
Activation separates into S-M and E

## Slide 30: Mugi Nonlinear Mapping
Value reuse
Precomputed LUT loads from iSRAM
Window selected

## Slide 31: Mugi Nonlinear Mapping
Mantissa temporal subscription
Compute array subscribes to LUT values with S-M

## Slide 32: Mugi Nonlinear Mapping
Exponent temporal subscription

## Slide 33: Mugi Nonlinear Mapping
Additional vector operations and storing
i.e. softmax accumulation

## Slide 34: Results
Nonlinear
GEMM
End-to-end

## Slide 35: Iso-Area Nonlinear and GEMM
Carat: Previous VLP work
SA: Systolic Array
SD: SIMD Array
-F: Figna INT-FP multiplier
SM: Softmax
T: Tensor core
VA-FP: Precise vector array
VA-AP: Approximate vector array
Notes: Nonlinear
Memory bandwidth limits the vector array
Other approximations have longer per operator compute time, where we are pure lookup, significantly increasing efficiency
Gemm
Similar trends, but smaller difference
Gain comes from lack of additional vector unit (eff)
Full utilization at small batch size

## Slide 36: Iso-Throughput Batch Size Study
Carat: Previous VLP work
SA: Systolic Array
SD: SIMD Array
-F: Figna INT-FP multiplier
Notes: Mugi saturates at 8 vs saturates at 16 (SA/SD 16)
Values are overlapping as the throughput is the same

## Slide 37: Q & A